Hardware Requirements Specification (HRS)
E1001 Carrier PCBA
David D. Clark
October 15, 2024
Revision History
Revision	Date	Changes
X1		Initial draft.

# Reference Documents
Document	Source

Raspberry Pi CM4 datasheet	https://datasheets.raspberrypi.com/cm4/cm4-datasheet.pdf
USB 2.0 Standard

# Definitions and Acronymse
Acronyms
CM4	Raspberry Pi Compute Module 4
POE	Power Over Ethernet
SoM	System on module
TVS	Transient Voltage Suppresion
UPS	Uninterruptible Power Supply
USB	Universal Serial Bus

Definitions

# Introduction
The hardware requirements for the  E1001Carrier PCBA are described in this document. The intent is to capture the minimum set of requirements to ensure that the board will preform as expected in the context of the KG-VRS project. The E1001 Carrier PCBA will meet the requirements described in this document. However the E1001 Carrier PCBA may included features in addition to those described in this document.
# PCBA Description
General description of the board being specified.
# Block Diagram

# Requirements
## Power

## Power Inputs
Requirement	Description	Reference
	The E1001 Carrier PCBA shall accept a voltage input range of 5 VDC to 24 VDC.
	The E1001 Carrier PCBA shall provide a cricuit for reverse polarity protection on the DC input.
	The E1001 Carrier PCBA shall provide a fuse on the DC input for over current protection.
	The E1001 Carrier PCBA shall provide a circuit to indicate that the over current protection fuse has failed.
	The E1001 Carrier PCBA shall provide TVS suppression on the DC input.
	The E1001 Carrier PCBA shall provide a common mode choke on the main voltage input.
	The E1001 Carrier PCBA shall provide an Ethernet interface capable of POE.

## Derived Power Rails
Requirement	Description	Reference
	The E1001 Carrier PCBA shall provide a 5 VDC power rail.
	The E1001 Carrier PCBA 5 VDC rail shall be capable of sourcing xx A
	The E1001 Carrier PCBA shall provide a 3.3 VDC rail
	The E1001 Carrier PCBA 3.3 VDC rail shall be capable of sourcing xx A.

## Grounding
Requirement	Description	Reference
	The E1001 Carrier PCBA shall have a single point ground.
	The E1001 Carrier PCBA single point ground shall be located on the input to the power conditioning common mode choke.	E1001:REQ:4.2.6
	The E1001 Carrier PCBA analog and digital signals shall be referenced to the output of the common mode choke.	E1001:REQ:4.2.6
	The E1001 Carrier PCBA derived power rails shall be referenced to the output of the common mode choke.	E1001:REQ:4.2.6

## Power Outputs
Requirement	Description	Reference
	The E1001 Carrier PCBA shall provide a 12 VDC output.
	The E1001 Carrier PCBA shall provide 5 VDC at 1 A to each of the USB 2.0 module interfaces.

## MCU
Requirement	Description	Reference
	The E1001 Carrier PCBA shall use a Raspberry Pi Compute Module 4 CM410802 as the SoM.
	The E1001 Carrier PCBA shall be capable of of flashing an image to the eMMC storage of the Raspberry Pi CM4 using an external host computer.

## GPIO
Requirement	Description	Reference
	The E1001 Carrier PCBA shall expose nn GPIO pins.
	The exposed GPIO pins shall be 5V tolerant.

## Communication
Requirement	Description	Reference
	The E1001 Carrier PCBA shall expose the Ethernet port on the Raspberry Pi CM4.
	The E1001 Carrier PCBA shall expose the USB 2.0 bus on the Raspberry Pi CM4.

## Peripherals
Requirement	Description	Reference

## Mechanical
Requirement	Description	Reference

## User Interface
Requirement	Description	Reference

## GPIO Connector
Requirement	Description	Reference
	The E1001 Carrier PCBA shall provide an external GPIO connector for the exposed GPIO pins on the Raspberry Pi CM4.	E1001:REQ:4.7.1
	The E1001 Carrier PCBA GPIO connector shall provide at least one +12VDC output pin.	E1001:REQ:4.7.3
	The E1001 Carrier PCBA GPIO connector shall provide a ground pin for each GPIO pin.

## USB Module Interfaces
Requirement	Description	Reference
	The E1001 Carrier PCBA shall provide interface circuits for four USB 2.0 based interface modules.
	The E1001 Carrier PCBA USB 2.0 interface modules shall use the same connector and the same pinout.
	The USB 2.0 output interface shall be capable of sourcing 1 A to each interface module.

## MMDVM Interface
Requirement	Description	Reference
	The E1001 Carrier PCBA shall provide an interface to accept a standard MMDVM PCBA

## UPS
Requirement	Description	Reference
	The E1001 Carrier PCBA shall provide a UPS circuit capable of running the Raspberry Pi CM4 after power has been lost from the main power input or the POE input.
	The UPS shall be capable of powering the E1001 Carrier PCBA for xx minutes.

## Feature
Requirement	Description	Reference

## Feature
Requirement	Description	Reference